## Slide 1
Plasticizer
Low-range water reducers, used in conventional applications, where regular w/c is used.
CHARACTERISTICS
Low range water reducers, which typically allow to work at w/c above 0.5.
Robust products which will support different types of raw materials (cement, aggregates).
Compatible with all other types of concrete admixtures, and typically used in combination with set admixtures.
VALUE PROPOSITION
  State-of-the-art admixtures
  Robust and reliable product
  Regular water reduction and workability retention
TECHNOLOGY
ISOPLAST
ISOFLEX

## Slide 2
Superplasticizer
High-range water reducers, used for special applications, where low w/c are required and extended workability retention.
CHARACTERISTICS
High range water reducers, which typically allow to work at w/c below 0.5.
Enables to produce low viscous concrete, with extended workability retention.
Specially recommended for all special products / VAPs such as Resilia, Evolution, Promptis, High Strength, ...
VALUE PROPOSITION
  Powerful and versatile products
  Designed for high strength and special applications
  Promotes high strength and low viscosity concrete
TECHNOLOGY
ISOFLOW

## Slide 3
Pre-Cast Admixtures
Admixtures designed for pre-cast applications, notably vibro-compacted elements
CHARACTERISTICS
High range water reducers, with controlled workability, and promoting high early strength.
Products also designed for vibro-compacted pre-cast elements, where the thixotropy and the compaction are key.
Could also be optimized with a surfactant to improve the surface quality after demolding.
VALUE PROPOSITION
  High early strength
  High water reduction
  Compatible with vibro-compaction
TECHNOLOGY
ISOCAST
ISOMAP

## Slide 4
Viscosity Modifyer
Products affecting the viscosity and thixotropy of the concrete.
CHARACTERISTICS
Admixtures to provide robustness to concrete towards variation of water and admixture dosage.
Prevents segregation and static segregation and reduces significantly the bleeding.
Can be used for special applications where high thixotropy is needed
Could be used for anti-washout application where the cohesion of concrete is critical
VALUE PROPOSITION
  Robustness and segregation/bleeding control
  Compatible with most of typical admixtures
  Recommended with ISOFLOW technology
  Liquid product
TECHNOLOGY
ISOSTAB
ISOSIL

## Slide 5
Set Retarder
Chemicals that affects the setting time and provides retardation
CHARACTERISTICS
Admixtures that control the hydration reactions and can extend the setting time.
Allows to extend the workability of concrete when the plasticizer/superplasticizer is not sufficient.
Broad range of chemistry that target different phases and parameters.
VALUE PROPOSITION
  Versatile and robust portfolio that covers all cements
  Extension of workability or “sleeping” concrete
  Can be combined with most admixtures
TECHNOLOGY
ISORETARD
ISOPAUSE
Increase
ISORETARD

## Slide 6
Accelerators
Admixtures used to accelerate the cement hydration, especially in cold conditions
CHARACTERISTICS
Chemicals or combination of chemicals to accelerate the cement hydration and mitigate the effect of cold temperature on the setting time and strength development.
Portfolio also includes non-chloride based products to prevent for rebar corrosion.
VALUE PROPOSITION
  Non-chloride based products available
  Increase of early strength.
  Compatible with typical plasticizers
TECHNOLOGY
Accel
ISOXEL

## Slide 7
Promptis Accelerator
Admixtures especially designed for Promptis Concrete
CHARACTERISTICS
Specifically developed for Promptis concrete, where ultra-high early strength is required.
Combination with ISOFLOW technology will allow to maintain long workability concrete for up to 3 hours.
No limitation with dosage.
VALUE PROPOSITION
  Ready-mix admixture
  No need to add the product at the job site
TECHNOLOGY
ISOXEL 860
ISOXEL 877

## Slide 8
Air Entrainer
Admixtures based on surfactant, to increase the air content of concrete
CHARACTERISTICS
Natural and synthetic surfactants used to increase the air content in concrete.
Typically used for Freeze and Thaw applications, to improve the durability.
Also provides higher stability to special concretes such as screeds and self-compacted concrete.
Also recommended to improve the surface finish of vibro-compacted pre-cast elements.
VALUE PROPOSITION
  Controlled air generation and air quality
  Short mixing time required at the batching plant
  Robust and reproducible.
TECHNOLOGY
ISOSPHERE

## Slide 9
Defoaming admixtures
Admixtures looking at controlling the air content of concrete
CHARACTERISTICS
Typically used when the integrated defoaming system of the plasticizer or superplasticizer do not provide the expected air content.
VALUE PROPOSITION
  Liquid product, ready to use
  Low dosage required – very efficient product
  Robust and versatile
TECHNOLOGY
ISODENSE

## Slide 10
Foaming System
Combination of foaming surfactant, with specific superplasticizers, to guarantee a high and stable air content.
CHARACTERISTICS
Specially designed surfactant based admixtures, to ensure a rapid air entrainment, in short mixing time.
Products also available for foam generator.
Recommended to use with specific ISOFLOW products for foam concrete.
VALUE PROPOSITION
  Liquid product, ready to use
  Stable air: no collapsing before setting
  Optimization of the air structure
TECHNOLOGY
ISOFOAM
ISOFLOW

## Slide 11
Water Repellent
Range of products used to provide water repellency or impermeability to concrete materials.
CHARACTERISTICS
Range of products to either give water-repellency or impermeabilization of concrete elements.
Can be used either in the bulk, or could also be applied as a surface post-treatment.
VALUE PROPOSITION
  Improved durability
  Avoids the formation of fungi and humidity
  Compatible with all other admixture types.
TECHNOLOGY
ISOFUGE

## Slide 12
Internal Curing
Unique range of products that promotes the internal curing of the concrete.
CHARACTERISTICS
Chemicals added in the concrete bulk, to prevent the drying during the initial curing of the concrete.
Maintains the level of water for the adequate hydration of the cement, by different means.
Specially recommended for screeds or industrial floors where joints and stress zones are typically leading to cracks
VALUE PROPOSITION
  Unique technology
  Economical: avoid post curing of the concrete
  Enhance the surface and the strength
TECHNOLOGY
ISOKHORE 120
ISOKHORE 1850
ISOKHORE 845

## Slide 13
Shrinkage Control
Typical products used to reduce the shrinkage during the curing and drying of the concrete.
CHARACTERISTICS
State-of-the-art technology that provides a surface tension reduction in the capillaries, during the curing of the concrete.
This reduces the internal forces which typically lead to crakcs.
The products will also reduce/suppress the curling effect at long term.
VALUE PROPOSITION
  Long term control – no curling
  Easy to use: dosed in the concrete bulk
  Robust: do not depend on the cement chemistry
TECHNOLOGY
ISOKHORE
ISOKHORE

## Slide 14
Corrosion Inhibitor
Admixtures used to prevent the corrosion of rebars and other metallic reinforcements.
CHARACTERISTICS
Redox chemical that will prevent the corrosion of the rebars and other metallic reinforcement.
This is particularly the case in aggressive environment such as sea/ocean proximity.
VALUE PROPOSITION
  Easy to use: dosed in the concrete bulk
  Robust: redox reaction will work with all chemical aggressions.
  Improvement of durability
TECHNOLOGY
ISOINHIBIT

## Slide 15
Flooring Plasticizer
Specific (super)platicizers for flooring applications, and notably industrial floors.
CHARACTERISTICS
Provides with the adequate water reduction and workability for the production and transport of the concrete, but prevents the re-fluidification during the surface finish.
Avoid the bleeding of the surface which could lead to delaminating of the floor.
Compatible with the typical hardening powders used for the surface finish.
VALUE PROPOSITION
  Easy to use: dosed as a regular admixtures
  Compatible with other admixture types
  Water reduction and workability can be adjusted based on the cement and needs.
  Support the early strength development
TECHNOLOGY
ISOFLOW 3740
ISOFLOOR

## Slide 16
Pervia Admixtures
Admixtures developed specifically for Pervia concrete, to enhance the cohesion of the concrete.
CHARACTERISTICS
Superplasticizer types products, which have been formulated with selected raw materials in order to provide with:
  Improved cohesion of the cement matrix with the aggregates
  Long workability retention
  Fast dispersion to prevent temperature increase during batching
VALUE PROPOSITION
  Concrete admixtures: used at the batching plant
  Can be optimized for all cements
  Regular dosages (0.5-1.5% bwoc)
  Compatible with other admixture types
TECHNOLOGY
ISOPERVIA

## Slide 17
RCC Admixtures
Portfolio of admixtures designed for the production, transport, placing and curing of Roller Compacted Concrete.
CHARACTERISTICS
Portfolio of admixtures to address the different needs of Roller Compacted Concrete.
Plasticizers and retarders to improve the workability and compaction
Compaction aids to increase the performances
Curing aids to prevent for the fast drying of the concrete, and improve the surface finish during the paving.
VALUE PROPOSITION
  Robust and versatile: products can be adjusted for each cements
  Covers all the typical needs for RCC
  All products are dosed at the production plant
TECHNOLOGY
ISOVIA

## Slide 18
Fair Face
Specific products used to suppress the air bubbles on the surface of concrete.
CHARACTERISTICS
Liquid product dosed in the concrete to reduce significantly the formation of bubbles and holes on the surface of concrete.
This product is recommended for fair face concrete and architectonic walls.
It does not impact the fresh or the hard performances of the concrete
VALUE PROPOSITION
  Easy to use: typical dosage of 1 kg/m3 dosed at the RMX plant
  Do no require any additional preparation of the formwork
  Synergy effect with the demolding oil
TECHNOLOGY
ISOGLASS

## Slide 19
Color Enhancer
Admixtures used to enhance the color durability and prevents carbonatation and efflorescence.
CHARACTERISTICS
Liquid admixtures used in the concrete bulk, when colors and pigments are used, in order to reduce the whitening effect due to the carbonatation and/or efflorescence.
Can be as well applied on the fresh concrete to provide as well with a shiny appearance.
Does not retard the setting or the strength
VALUE PROPOSITION
  Robust: works with all colors
  Compatible with most of the cements
  Provides as well a water-repellent effect for durability
TECHNOLOGY
ISOFUGE 220